# Objects in the Project
## General MVC knowledge
The controller is the function that marshalls all views against the model.
Only the model persists data.
The model must be rigorously monitored (in design) to be only minimum/sufficient ... as little derived as possible.
The model must minimize the duplicaiton of data.
The model must not span objects/subjects that are completely disjoint.
display(view & controller) and analyzer(a complicated control) ask model about how to work

# Human and machine Factors
Vertical has display as dB and as direct value.
Horizontal has only direct value.
Direct value can have linear and log gridding.
dB only makes sense to have linear gridding.
Negative amplitude only makes sense in re/im or the phase of rad/th
No human should be asked to squint to a grid spacing smaller than 50 pixels.
That says that the 1/2/5 means that the biggest pixel spacing will be 100. Maybe We'll See.
*/
/*
==== Grid factors
  dB/Lin (but we won't even begin to address this for now.
  Number of span pixels on the screen
  Number of span grids on the screen
  IMPORTANT let the user operate in a freq/per/grid mode And then the span will become constrained by grid size pixel norms.

Center-span Mode - set the mid -- set the span -- top/bottom are derived -- grids need ferreting out.
  Top-span Mode - set the top -- set the span -- bottom is derived, center is irrelevant -- grids need ferreting out.
  Bottom-span Mode - set the bottom -- set the span -- top is derived, center is irrelevant -- grids need ferreting out.
  Ends Mode - set the top -- set the bottom -- span is derived, center is irrelevant -- grids need ferreting out.
        If center is off of 1/2/5/ then draw a light line at the center and always keep 1/2/5 drawn dark (if center is setting)
        span means either top-bottim OR x per grid
        allow arbitrary x per grid

# Nomenclature
start	Lowest freq, at the left end of the screen
center	Center freq, at the equilateral middle of the view screen. Not relevant in Log
stop	Highest freq, at the right edge of the screen
span	The difference between the right edge and the left edge (Hz or decades, whole number decades maybe needs to be enforced, not whole numbers of grids)
top	Highest amplitude, top edge of the view screen
center	Just like frequency, also not relevant in Log display mode.
bottom	Lowest amplitude, bottom edge of the view screen
magnification	Ratio of frequency points to pixel points to be displayed.

# Sampled Domain Tutorial
There are three sampled domains, the time signal, the frequency signal and the screen dots.

Time Signal is all taken care of in ScopeVert. Watch out for the end times when the scope display demand is not the same length of samples as the freq analysis demand.

Frequency Signal is defined here. It is the array of values from the time-to-frequency transform operation. There are a few problems to solve.
Apodization needs to be handled here, but applied to time array, so those samples properties are relevant.
Short sequences use DFT and long sequences use FFT.
Currently either goes above 2048 and it bops to FFT with 2k as the only legal vector length.
In the future, allow the user to spec the time DFT/FFT explicitly.
Both DFT and FFT have N time elements generally not exactly displayed over in the scope. Some future revision of chert will highlite the portion of the time display that yields the frequency anlysis.
The real vs re/im thing needs implementation.

The fastest way to analyze a time signal is with an equal number of complex sinusoids from DC to the nyquist frequency.
The sub-range frequency analysis thing hasn’t been addressed, but takes massive functionaity to dig out a sub-range and just get the transform of that. This can’t be done in time domain straight away. Generally, you need to get a longer time-length starting vector to get the big number of samples for the fine-frequency sub-range to be looked at. It has to be:
  - brick-wall filtered on the big big time function.
  - modulated down to baseband.
  - decimated (more formally resampled/down-sampled)
  - re-spec-an’d with the offset range spec fed to the display for accurate gridding and scaling.

The way to take frequency-domain-quantized data to present as pixel-domain-gridded (interpolate/decimate) you can:
- sinc() - purists like this.
- Zero-order hold, pretty common, still has a question of choosing. Start of pixel-span … end of pixel span … center of pixel span … This comes for free (last sample in pixel-span) when you use the draw functiion straigh-away WHEN you are in more-freq-than-pixel magnification.
- linear interpolate … This comes for free if you use the draw function straight-away WHEN you are in more-pixel-than-freq magnification.
- [min|max|average] even with stdev bars, all 3 or only one. Pretty compute intensive per pixel but yields LOTS of information.
- WARNING - using draw function straight-away might way over-tax compute demands as you draw a bunch of deely sub-pixel frequency spannings all onto one pixel.
- When there are lots more pixels than frequency objects … well … all thes above discussions are still valid.

# Other Stuff
For I|Q signals …
near-carrier phase noise. All of hematite is working on this right now.
but actually you'd really want to see pos-neg asymmetries, now wouldn't you. Pos/neg overlay! Patent it! Invented Thurs 2010-10-24 8:05 Central DST Time, US, Van Alstyne TX 75495.
For a stated carrier, and a stated bandwidth, use some kind of technique (time or frequency) to derive “twist” of the signal. This is super-relevant for data signals where a right-hand or left-hand procession around the grid of digital data nexus locations FEELS like a carrier offset.
 - coherent-carrier demodulated down to DC (but we have to synthesize the carrier frequency) just doesn't make sense as log.
 - broadband baseband stuff ... audio channels, noise-floor analysis, impulse responses. Can be log or linear and only makes sense
as Real in the time domain stuff.
 - But damn, what about a really cool filter that has a complex component, Hilbert kind of stuff. Linear or log+flipped.

OK, so that answers it. I will have a Log with Complex then a Flip and an overlay of flipped/unflipped! Like I said above
Patent it.
 - Linear -- { (start,center) | (start,stop) | (center,stop) | (start,span) | (center,span) | (stop,span) }
 - Log -- { (start,stop) | (start|decades) | (stop|decades) }

Persistance:
 - Linear --
 - Log --
*/